## Slide 1: Microprogrammed Control
1

## Slide 2: Contents
  4.1 Introduction: Hardwired and Microprogrammed Control Unit, Control Word, Microprogram, Control Memory, Control Address Register, Sequencer,
  4.2 Address Sequencing: Conditional Branch, Mapping of Instructions, Subroutines, Microinstruction Format, Symbolic Microinstructions
  4.3 Design of Control Unit: Decoding, Microprogram Sequencer.
2

## Slide 3: Control Unit
3
Control unit generates timing and control signals for the operations of the computer.
It’s the part of the CPU that initiates sequences of microoperations.
It tells the computers memory ,arithmetic and logic unit and I/O devices how to respond to a programs instructions.
Two methods to implement the control unit:
Hardwired Control Unit:(uses fixes instructions, combinational logic
units of AND/OR(logic gates),encoders, decoders, etc.)
Microprogrammed Control Unit:(the logic of the control unit is specified by microprograms (consists of a sequence of instructions that specify microoperations).
Note: refer unit-3 for more details.

## Slide 4: Terminology
Microprogram
Program stored in memory that generates all the control signals required to execute the instruction set correctly.
Consists of microinstructions
Microinstruction
Contains a control word and a sequencing word
  Control Word - All the control information required for one clock
cycle. Or
    The control variables at any time are represented by 1’s and 0’s knows as control word.
    Control words can be programmed to perform various operations.
    Sequencing Word -Information needed to decide the next microinstruction address.

## Slide 5: Microoperations
In computer central processing units, micro-operations (also known as a micro-ops or µops) are detailed low-level instructions used in some designs to implement complex machine instructions (sometimes termed macro- instructions in this context).
Microcode
Microinstructions can be saved by employing subroutines that use common
sections of microcode.
For example, the sequence of micro operations needed to generate the effective address of the operand for an instruction is common to all memory
reference instructions.
This sequence could be a subroutine that is called from within many other routines to execute the effective address computation.
5

## Slide 6: Control memory (control storage: CS)
6
Storage in the microprogrammed control unit to store the microprogram.
Each word in control memory contains within it a microinstruction.
Writeable control memory (writeable control storage: WCS)
Control Storage whose contents can be modified, allow the change in microprogram and Instruction set can be changed or modified is referred as Writeable Control Memory.
Dynamic microprogramming
Permits a microprogram to be loaded initially from an auxiliary memory
such as a magnetic disk.
Computer system whose control unit is implemented with a microprogram in WCS.
- Microprogram can be changed by a systems programmer or a user,
though it is mostly used for reading.

## Slide 7
Sequencer (Microprogram Sequencer)
A Microprogram Control Unit that determines the Microinstruction Address to be executed in the next clock cycle (next address generator is called sequencer)
  In-line Sequencing
  Branch
  Conditional Branch
  Subroutine
  Loop
  Instruction OP-code mapping

## Slide 8
Figure : Microprogrammed control organization.
The general configuration of a microprogrammed control unit is demonstrated in the block diagram

## Slide 9
The general configuration of a micro-programmed control unit is demonstrated in the block diagram of Figure.
The control memory is assumed to be a ROM, within which all control
information is permanently stored.
The microinstruction contains a control word that specifies one or more microoperations for the data processor. Once these operations are executed, the control must determine the next address.
The location of the next microinstruction may be the one next in sequence, or it may be located somewhere else in the control memory.
While the microoperations are being executed, the next address is
computed in the next address generator circuit and then transferred into the control address register to read the next microinstruction.

## Slide 10
Thus a microinstruction contains bits for initiating microoperations in the data processor part and bits that determine the address sequence for the control memory.
The next address generator is sometimes called a micro-program
sequencer, as it determines the address sequence that is read from control memory.
Typical functions of a micro-program sequencer are incrementing the control address register by one, loading into the control address register an address from control memory, transferring an external address, or loading an initial address to start the control operations.
The control data register holds the present microinstruction while the next
address is computed and read from memory.

## Slide 11: Address sequencing
Instruction code
Mapping
logic
Multiplexers
Control memory (ROM)
Subroutine register (SBR)
Branch logic
Status bits
Microoperations
Control address register
(CAR)
Incrementer
MUX
select
select a status
bit
Branch address
Figure : Selection of Address for control memory.

## Slide 12: Address Sequencing
12
Microinstructions are stored in control memory in groups, with each group specifying a routine.
To appreciate the address sequencing in a micro-program control unit, let us
specify the steps that the control must undergo during the execution of a single
computer instruction.
Step-1:
An initial address is loaded into the control address register when power is turned on in the computer.
This address is usually the address of the first microinstruction that activates the instruction fetch routine.
The fetch routine may be sequenced by incrementing the control address register
through the rest of its microinstructions.
At the end of the fetch routine, the instruction is in the instruction register of the
computer.

## Slide 13: Step-2:
13
The control memory next must go through the routine that determines the effective address of the operand.
A machine instruction may have bits that specify various addressing modes,
such as indirect address and index registers.
The effective address computation routine in control memory can be reached through a branch microinstruction, which is conditioned on the status of the mode bits of the instruction.
When the effective address computation routine is completed, the address of the operand is available in the memory address register.
Step-3:
The next step is to generate the microoperations that execute the instruction fetched from memory.
The microoperation steps to be generated in processor registers depend on the
operation code part of the instruction.

## Slide 14
Each instruction has its own micro-program routine stored in a given location of control memory.
The transformation from the instruction code bits to an address in control memory where the routine is located is referred to as a mapping process.
A mapping procedure is a rule that transforms the instruction code into a control memory address.
Step-4:
Once the required routine is reached, the microinstructions that execute the instruction may be sequenced by incrementing the control address register.
Micro-programs that employ subroutines will require an external register for storing the return address.
Return addresses cannot be stored in ROM because the unit has no writing capability.

## Slide 15
When the execution of the instruction is completed, control must return to the fetch routine.
This is accomplished by executing an unconditional branch microinstruction to the first address of the fetch routine.

## Slide 16
In summary, the address sequencing capabilities required in a control memory are:
Incrementing of the control address register.
Unconditional branch or conditional branch, depending on status bit
conditions.
A mapping process from the bits of the instruction to an address for
control memory.
A facility for subroutine call and return.

## Slide 17: Steps in Selection of Address
Conditional Branch
Branching from one routine to another depending on status bit conditions.
If Condition is true, then Branch (address from the next address field of the
current microinstruction) else Fall Through
Conditions to Test: O(overflow), N(negative),Z(zero), C(carry), etc.
Unconditional Branch
Fixing the value of one status bit at the input of the multiplexer to 1

## Slide 18: Mapping of instructions Direct Mapping OP-codes of Instructions
ADD Routine
AND Routine
LDA Routine
STA Routine
BUN Routine
Control Storage
ADD | 0000
AND | 0001
LDA | 0010
STA | 0011
BUN | 0100
.
.
.
Address
0000
0001
0010
0011
0100
Address
10 0000 010
10
0001
010
10 0010 010
10 0011 010
10 0100 010
Mapping
Bits
10
xxxx
010
ADD Routine
AND Routine
LDA Routine
STA Routine
BUN Routine

## Slide 19: Mapping of instructions to micro-routines
Mapping bits Microinstruction
address
Mapping function implemented by ROM or PLA
OP-code
Mapping memory
(ROM or PLA)
Control address register
Control Memory
1 | 0 | 1 | 1 | Address
OP-code
0 | x x x x | 0 0
0 1 0 1 1 0 0 |  | 
Machine Instruction
Mapping from the OP-code of an instruction to the address of the Microinstruction which is the starting microinstruction of its execution microprogram

## Slide 20
Subroutines
Subroutines are programs that are used by other routines to accomplish a particular task. A subroutine can be called from any point within the main body of the microprogram.
For example, the sequence of microoperations needed to generate the effective address of the operand for an instruction is common to all memory reference instructions. This sequence could be a subroutine that is called from within many other routines to execute the effective address computation.
The subroutine register can then become the source for transferring the
address for the return to the main routine.
The best way to structure a register file that stores addresses for subroutines is to organize the registers in a last-in, first-out (LIFO) stack

## Slide 21: Microprogram Example
Once the configuration of a computer and its microprogrammed control unit is established, the designer's task is to generate the microcode for the control memory. This code generation is called microprogramming and is a process similar to conventional machine language programming.
To appreciate this process, we present here a simple digital computer and show how it is microprogrammed
Computer Configuration

## Slide 22
MUX
AR
10 0
PC
10 0
Address
Memory 2048 x 16
MUX
DR
15
0
Arithmetic logic and shift unit
15 0
AC
6 0
SBR CAR
6
0
Control memory
128 x 20
Control unit
Figure: Computer hardware configuration.

## Slide 23
Consists of two memory units: a main memory for storing instructions and
data, and a control memory for storing he microprogram.
Four register are associated with the processor unit and two with the control
unit.
The processor registers are program counter PC, address register AR, data register DR, and accumulator register DR, and accumulator register AC. The function of these registers is similar to the basic computer.
The control unit has a control address register CAR and a subroutine register SBR.
The control memory and its registers are organized as a micro programmed
control unit.
The transfer of information among the register in the processor is done through multiplexers rather than a common bus.

## Slide 24
DR can receive information from AC, PC, or memory.
AR can receive information from PC or DR, PC can receive information only from AR.
The arithmetic, logic, and shift unit performs microoperations with data
from AC and DR and places the result in AC.
Note that memory receive its address from AR. Input data written to memory come from DR, and data read from memory can go only to DR.

## Slide 25: Microinstruction Format
Figure : Micro-instructions code format (20 bits).
F1 | F2 | F3 | CD | BR | AD
3
3
3
2
2
7
F1, F2, F3: Microoperation fields CD: Condition for branching BR: Branch field
AD: Address field

## Slide 26
The microinstruction format for the control memory is shown in figure . The 20 bits of the microinstruction are divided into four functional parts as follows:
  The three fields F1, F2, and F3 specify microoperations for the computer. The microoperations are subdivided into three fields of three bits each. The three bits in each field are encoded to specify seven distinct microoperations. This gives a total of 21
microoperations.
  The CD field selects status bit conditions.
  The BR field specifies the type of branch to be used.
  The AD field contains a branch address. The address field is
seven bits wide, since the control memory has 128 = 27 words.

## Slide 27: Microinstruction field descriptions – F1,F2,F3
F1 | Microoperation | Symbol
000 | None | NOP
001 | AC  AC + DR | ADD
010 | AC  0 | CLRAC
011 | AC  AC + 1 | INCAC
100 | AC  DR | DRTAC
101 | AR  DR(0-10) | DRTAR
110 | AR  PC | PCTAR
111 | M[AR]  DR | WRITE
F2 | Microoperation | Symbol
000 | None | NOP
001 | AC  AC - DR | SUB
010 | AC  AC  DR | OR
011 | AC  AC  DR | AND
100 | DR  M[AR] | READ
101 | DR  AC | ACTDR
110 | DR  DR + 1 | INCDR
111 | DR(0-10)  PC | PCTDR
F3 | Microoperation | Symbol
000 | None | NOP
001 | AC  AC  DR | XOR
010 | AC  AC’ | COM
011 | AC  shl AC | SHL
100 | AC  shr AC | SHR
101 | PC  PC + 1 | INCPC
110 | PC  AR | ARTPC
111 | Reserved | 

## Slide 28: Microinstruction field descriptions – CD,BR
CD | Condition | Symbol | Comments
00 | Always = 1 | U | Unconditional branch
01 | DR(15) | I | Indirect address bit
10 | AC(15) | S | Sign bit of AC
11 | AC = 0 | Z | Zero value in AC
BR | Symbol | Function
00 | JMP | CAR  AD if condition = 1 CAR  CAR + 1 if condition = 0 CAR  AD, SBR  CAR + 1 if condition = 1 CAR  CAR + 1 if condition = 0 CAR  SBR (Return from subroutine) CAR(2-5)  DR(11-14), CAR(0,1,6)  0
01 | CALL | 
10 | RET | 
11 | MAP | 

## Slide 29: Symbolic Microinstructions
Symbols are used in microinstructions as in assembly language.
A symbolic microprogram can be translated into its binary equivalent by a microprogram assembler.
Sample Format
Five fields:
label ; micro-ops ; CD ; BR ; AD
Label:
may be empty or it may specify a symbolic address terminated with a colon (:).
Micro-ops: consists of one, two, or three symbols separated by commas CD: one of {U, I, S, Z}, where U: Unconditional Branch
I: Indirect address bit
S: Sign of AC
Z: Zero value in AC

## Slide 30: BR: contains one of {JMP, CALL, RET, MAP} AD: specifies a value for the address field of the microinstructions in one of three possible ways :
30
With a symbolic address, which must also appear as a label.
With the symbol NEXT to designate the next address in sequence.
When the BR field contains a RET or MAP symbol, the AD field is left empty and is converted to seven zeros by the assembler.

## Slide 31: Symbolic microprogram - fetch routine
During FETCH, Read an instruction from memory and decode the
instruction and update PC.
Sequence of microoperations in the fetch cycle:
AR PC
DR M[AR], PC  PC + 1
AR  DR(0-10), CAR(2-5)  DR(11-14), CAR(0,1,6)  0

## Slide 32
The translation of the symbolic microprogram to binary produces the following binary microprogram.
Binary
address | F1 | F2 | F3 | CD | BR | AD
1000000 | 110 | 000 | 000 | 00 | 00 | 1000001
1000001 | 000 | 100 | 101 | 00 | 00 | 1000010
1000010 | 101 | 000 | 000 | 00 | 11 | 0000000
Symbolic microprogram for the fetch cycle:
FETCH:
ORG 64 |  | 
PCTAR | U | JMP NEXT
READ, INCPC | U | JMP NEXT
DRTAR | U | MAP

## Slide 33
Control Storage: 128 20-bit words
The first 64 words: Routines for the 16 machine instructions
The last 64 words: Used for other purpose (e.g., fetch routine and
other subroutines)
Mapping: OP-code XXXX into 0XXXX00, the first address for the 16 routines are 0(0 0000 00), 4(0 0001 00), 8, 12, 16, 20, ..., 60

## Slide 34: Partial Symbolic Microprogram
Label | Microops | CD | BR | AD
 | ORG 0 |  |  | 
ADD: | NOP | I | CALL | INDRCT
 | READ | U | JMP | NEXT
 | ADD | U | JMP | FETCH
 | ORG 4 |  |  | 
BRANCH: | NOP | S | JMP | OVER
 | NOP | U | JMP | FETCH
OVER: | NOP | I | CALL | INDRCT
 | ARTPC | U | JMP | FETCH
 | ORG 8 |  |  | 
STORE: | NOP | I | CALL | INDRCT
 | ACTDR | U | JMP | NEXT
 | WRITE | U | JMP | FETCH
 | ORG 12 |  |  | 
EXCHANGE: | NOP | I | CALL | INDRCT
 | READ | U | JMP | NEXT
 | ACTDR, DRTAC | U | JMP | NEXT
 | WRITE | U | JMP | FETCH
 | ORG 64 |  |  | 
FETCH: | PCTAR | U | JMP | NEXT
 | READ, INCPC | U | JMP | NEXT
 | DRTAR | U | MAP | 
INDRCT: | READ | U | JMP | NEXT
 | DRTAR | U | RET | 

## Slide 35: The execution of the ADD instruction is carried out by the microinstructions at addresses 1 and 2. The first microinstruction reads the operand from memory into DR . The second microinstruction performs an add microoperation with the content of DR and AC and then jumps back to the beginning of
35
the fetch routine.
Binary Microprogram
The symbolic microprogram is a convenient form for writing microprograms in a way that people can read and understand. But this is not the way that the microprogram is stored in memory.
The symbolic microprogram must be translated to binary either by means of an assembler program or by the user if the microprogram is simple
enough.

## Slide 36: Binary microprogram
Micro Routine | Address Binary Microinstruction |  |  |  |  |  |  | 
 | Decimal | Binary | F1 | F2 | F3 | CD | BR | AD
ADD | 0 | 0000000 | 000 | 000 | 000 | 01 | 01 | 1000011
 | 1 | 0000001 | 000 | 100 | 000 | 00 | 00 | 0000010
 | 2 | 0000010 | 001 | 000 | 000 | 00 | 00 | 1000000
 | 3 | 0000011 | 000 | 000 | 000 | 00 | 00 | 1000000
BRANCH | 4 | 0000100 | 000 | 000 | 000 | 10 | 00 | 0000110
 | 5 | 0000101 | 000 | 000 | 000 | 00 | 00 | 1000000
 | 6 | 0000110 | 000 | 000 | 000 | 01 | 01 | 1000011
 | 7 | 0000111 | 000 | 000 | 110 | 00 | 00 | 1000000
STORE | 8 | 0001000 | 000 | 000 | 000 | 01 | 01 | 1000011
 | 9 | 0001001 | 000 | 101 | 000 | 00 | 00 | 0001010
 | 10 | 0001010 | 111 | 000 | 000 | 00 | 00 | 1000000
 | 11 | 0001011 | 000 | 000 | 000 | 00 | 00 | 1000000
EXCHANGE | 12 | 0001100 | 000 | 000 | 000 | 01 | 01 | 1000011
 | 13 | 0001101 | 001 | 000 | 000 | 00 | 00 | 0001110
 | 14 | 0001110 | 100 | 101 | 000 | 00 | 00 | 0001111
 | 15 | 0001111 | 111 | 000 | 000 | 00 | 00 | 1000000
FETCH | 64 | 1000000 | 110 | 000 | 000 | 00 | 00 | 1000001
 | 65 | 1000001 | 000 | 100 | 101 | 00 | 00 | 1000010
 | 66 | 1000010 | 101 | 000 | 000 | 00 | 11 | 0000000
INDRCT | 67 | 1000011 | 000 | 100 | 000 | 00 | 00 | 1000100
 | 68 | 1000100 | 101 | 000 | 000 | 00 | 10 | 0000000

## Slide 37: Design of control unit
3 x 8 decoder
7 6 5 4 3 2 1 0
F1
3 x 8 decoder
7 6 5 4 3 2 1 0
F2
3 x 8 decoder 7 6 5 4 3 2 1 0 |  |  |  |  |  |  |  | 
F3
Arithmetic logic and shift unit
AND
ADD
DRTAC
AC
Load
From From
PC DR(0-11)
Select
0 1
Multiplexers
AR
Load
Clock
AC
DR
DRTAR
PCTAR
Figure : Decoding of Microoperation Fields.

## Slide 38
38
The bits of the microinstruction are usually divided into fields, with each field defining a distinct, separate function.
Figure shows the three decoders and some of the connections that must be made from their outputs. Each of the three fields of the microinstruction presently available in the output of control memory are decoded with a 3 × 8 decoder to provide eight outputs.
From F1 =7 outputs, F2=7 outputs and F3=6 outputs total 20 outputs from decoder.
For example, when F1 = 101 (binary 5), the next clock pulse transition transfers the content of DR (010) to AR (symbolized by DRTAR).
Similarly, when F1 = 110 (binary 6) there is a transfer from PC to AR (symbolized by PCTAR).
outputs 5 and 6 of decoder F1 are connected to the load input of AR so that
when either one of these outputs is active, information from the multiplexers is
transferred to AR.

## Slide 39
39
The multiplexers select the information from DR when Output 5 is active and from PC when output 5 in inactive. The transfer into AR occurs with a Clock pulse transition only when output 5 or output 6 of the decoder are active.
The other outputs of the decoders that initiate transfers between registers
must be connected in a similar fashion.
The arithmetic logic shift unit can be designed Instead of using gates to generate the control signals marked by the symbols AND, ADD, and DR,
, these inputs will now come from the outputs of the decoders associated
with the symbols AND, ADD, and DRTAC.

## Slide 40: Microprogram sequencer
S1
3 2 1 0
MUX 1
External (MAP)
SBR
Load
Incrementer
CAR
Input logic
I0
MUX 2
Select
1
I S Z
Test
Clock
Control memory
Microops
CD
BR
AD
L
I1 T
S0
. . .
. . .
Figure : Microprogram sequencer for a control memory.

## Slide 41
The submit of the micro programmed control unit which presents an address to the control memory is called microprogram sequencer.
The input logic circuit has three inputs, I0, I1, and T, and three outputs, S0, S1 and L. variables S0 and S1 select one of the source addresses for CAR.
Variable L enables the load input in SBR. The binary values of the two selection variables determine the path in the multiplexer.
Four inputs to the MUX 1 ,select one address and store into CAR. MUX 2
test the value of selected status bit and result to input logic circuit.
For example, with S1 S0 = 10, multiplexer input number 2 is selected and establishes a transfer path from SBR to CAR.
Note that each of the four inputs as well as the output of MUX 1 contains a 7- bit address.
The truth table for the input logic circuit is shown in the table. inputs I1 and I0
are identical to the bit values in the BR field.

## Slide 42
The bit values for S1 and S0 are determined from the stated function and the path in the multiplexer that establishes the required transfer.
The subroutine register is loaded with the incremented value of CAR during a call microinstruction (BR = 01) provided that the status bit condition is satisfied (T = 1). The truth table can be used to obtain the simplified Boolean functions for the input logic:
S1 = I1
S0 = I1I0 + I1’T L = I1’I0T

## Slide 43
BR Field | Input I1I0T | MUX S1S0 | 1 | Load SBR L
0 0 | 000 | 00 | 0 | 
0 0 | 001 | 01 | 0 | 
0 1 | 010 | 00 | 0 | 
0 1 | 011 | 01 | 1 | 
1 0 | 10x | 10 | 0 | 
1 1 | 11x | 11 | 0 | 
Table : Input logic truth table for microprogram sequencer.