## Slide 1
Computer Arithmetic

## Slide 2
Contents
Introduction
Addition and Subtraction
Multiplication Algorithms
Division Algorithms

## Slide 3
Arithmetic instructions in digital computers manipulate data to produce results necessary for the solutions of computational problems. These instructions perform arithmetic calculations and are responsible for the bulk of activity involved in processing data in a computer.
The four basic arithmetic operations are addition,subtraction,multiplication and division.
From these four basic operations , it is possible to formulate other arithmetic functions and solve problems by means of numerical analysis methods.
An arithmetic processor is the part of a processor unit that executes arithmetic operations.
An arithmetic instruction may specify binary or decimal data, and in each case the data may be in fixed-point or floating point form.
Negative numbers may be in signed magnitude or signed compliment representation.
Fixed point numbers may represents integers or fractions.
Introduction

## Slide 4
The addition and subtraction algorithm for data represented in signed magnitude and again data represented in signed 2’s complement.
It is important to realize that the adopted representation for negative numbers refers to the representation of numbers in the register before and after the execution of the arithmetic operations.
Addition and Subtraction with Signed-magnitude Data:
The representation of numbers in signed-magnitude is familiar because it is used in everyday arithmetic calculations. The procedure for adding or subtracting two signed binary numbers with paper and pencils simple and straight-forward. A review of this procedure will be helpful for deriving the hardware algorithm.
When two numbers A and B are signed numbers are added or subtracted, we find that there are eight different conditions to consider, depending on the sign of the numbers and the operation performed.
Addition and Subtraction

## Slide 5
These conditions are listed in the first column of the table below. The other column in the table show the actual operation to be performed with the magnitude of the numbers. The last column is needed to prevent negative zero.
In other words ,when two equal numbers are subtracted, the result should be +0 not -0.
The algorithms for addition and subtraction are derived from the table and can be stated as follows (the words inside parentheses should be used for the subtraction algorithm) Addition (subtraction) algorithm:
  when the signs of A and B are identical (different), add the two magnitude and attach the sign of A to the result.
  When the sign of A and B are different (identical),compare the magnitudes and subtract the smaller number from the larger .

## Slide 6
Table : Addition and Subtraction of Signed Magnitude Numbers

## Slide 7
Hardware implementation
To implement the two arithmetic operations with hardware, it is first necessary that the two numbers be stored in registers.
Let A and B be two registers that hold the magnitude of the numbers, and As and Bs be two flip-flops that hold the corresponding signs. The results of the operation may be transferred to a third register however, a saving achieved if the result is transferred into A and As . thus A and As together from an accumulator register.
Consider now the hardware implementation of the algorithms above.
  First, a parallel adder is needed to perform the micro operation A+B.
  second, comparator circuit is needed to establish if A>B, A=B, or A<B.
  third, two parallel subtractor circuits are needed to perform the micro operation A-B and B-A.
  The sign relationship can be determined from an exclusive-OR gate with As and Bs as inputs.

## Slide 8
The output carry is transferred to flip-flop E.
The complementer consists of exclusive-OR gates and the parallel adder consists of full adder circuit.
Figure : Hardware for signed magnitude addition and subtraction

## Slide 9
For addition: A=3 and B=2, add A+B
+3 0011
+2 0010
……………………
+5 0101
For subtraction: add A+B’ +1
+3 0011
-2 1110
……………………..
+1 00 01

## Slide 10
Hardware Algorithm
Figure : Flowchart for add and subtract operations

## Slide 11
The two signs As and Bs are compared by an exclusive-OR gate . If the output of the gate is 0, the signs are identical if it is 1, the signs are different.
The magnitudes are added with a micro operation EA ← A+B.. Where EA is a register that combines E and A . The carry in E after the addition constitutes an overflow if it is equal to 1 and transferred into the add overflow flip-flop AVF.
The two magnitudes are subtracted if the signs are different for an add operation or identical for a subtract operation.
The magnitudes are subtracted by adding A to the 2’s complement of B.
No overflow can occur if the numbers are subtracted to AVF is cleared to 0. A 1 in E, indicates that A ≥ B and the number in A is the correct result.
If this number is zero, the sign A, must be made positive to avoid a negative zero. A 0 in E indicates that A < B.
Examples : (+8) + (-3) = +5, (-8) +(-3)= -11, (+8) - (-3) = +11, (-8) - (-3) = -5

## Slide 12
Addition and Subtraction with Signed 2’s Complement Data
The left most bit of binary number represents the sign bit 0 for positive and 1 for negative. If the sign bit is 1, the entire the entire number is represented in 2’s compliment form (+33 is represented as 00100001 and -33 as 11011111. Note that 11011111 is the 2's complement of 00100001, and vice versa ).
The addition of two numbers in signed 2’s complement form consists of adding the number with the sign bits treated the same as the other bits of the number . A carry out of the sign bit position is discarded .
The subtraction consists of first taking the 2’s compliment of the subtrahend and then adding it to the minuend
When two numbers of n digits each are added and the sum occupies n+1 Digits, we say that an overflow occurred.
When the two carries are applied to an exclusive-OR gate, the overflow is detected when the output of the gate is equal to 1.

## Slide 13
Figure : Hardware for signed 2's complement addition and subtraction.
AC and BR are the registers to hold the numbers.
The leftmost bit in AC and BR represent the sign bits of the numbers.
The two sign bits are added or subtracted together with the other bits in the complementer and parallel adder.
The overflow flip flop V is set to 1 if there is an overflow. The output carry in this case is discarded.

## Slide 14
Figure : Algorithm for adding and subtracting numbers in signed-2's complement representation.
The sum is obtained by adding the contents of AC and BR.
The overflow bit V is set to 1 if the exclusive OR of the last two carries is 1, and it is cleared to 0 otherwise.
The subtraction operation is accomplished by adding the content of AC to the 2’s complement of BR. Taking the 2’s complement of BR has the effect of changing a positive number to negative, and vice versa.

## Slide 15
Multiplication Algorithms
Multiplication of two fixed point binary numbers in signed magnitude representation is done with paper and pencil of successive shift and add operation.
If the multiplier bit is a 1, the multiplicand is copied down; otherwise, zeros are copied down.
Signed Magnitude representation

## Slide 16
When multiplication is implemented in a digital computer, it is convenient to change the process slightly. First instead of providing register to store and add simultaneously as many binary numbers as there are bits in the multiplier , as it is convenient to provide an adder for the summation of only two binary numbers and successively accumulate the partial products in a register. Second instead of shifting the multiplicand to the left , the partial product is shifted to the right
The hardware for multiplication consists of the equipment shown in fig. plus two are more registers.
These registers are together with registers A and B.
The multiplier stored in the Q register and its sign in Qs The sequence counter SC is initially set to a number equal to the number of bits in the multiplier. The counter is decremented by 1 after forming each partial product
The sum of A and B forms a partial product which is transferred to the EA register .
Hardware Implementation for Signed Magnitude data

## Slide 17
Figure : Hardware for multiply operation.
The shift will be denoted by the statement shr EAQ to designate the right shift depicted .
The least significant bit of A is shifted into the most significant position of Q.

## Slide 18
Hardware Algorithm
Figure : Flowchart for multiply operation.
Initially the multiplicand is in B and the multiplier in Q there corresponding signs are in Bs and Qs .,respectively.
Register A and E are cleared and the sequence counter SC is set to a number equal to the number of bits of the multiplier.
After the initialization , the low order bit of the multiplier is in Qn is tested .if it is 1,the multiplicand In B is added to the present partial product in A . If it is 0, nothing is done .
Register EAQ shifted once to the right to form the new partial product.
The process stops when SC=0.
Note that the partial product formed in A is shifted into Q one bit at a time and eventually replaces multiplier. The final product is available in both A and Q,with A holding the most significant bits and Q holding the least significant bits.

## Slide 19
TABLE : Numerical Example for Binary Multiplier
Booth Multiplication Algorithm
Example: 23 x 19 = 437, B=10111 and Q=10011

## Slide 20
Signed 2’s complement representation
Booth algorithm gives a procedure for multiplying binary integers in signed 2’s complement representation.
It operates on the fact that strings of 0's in the multiplier require no addition but just shifting, and a string of 1's in the multiplier from bit weight 2k to weight 2m can be treated as 2k+1 – 2m.
For example, the binary number 001110 (+ 14) has a string of 1's from 23 to 21 (k = 3, m = 1). The number can be represented as 2k-1 - 2m = 24 – 21 = 16-2 = 14.
Therefore, the multiplication M x 14, where M is the multiplicand and 14 the multiplier, can be done as M x 24 - M X 21 Thus the product can be obtained by shifting the binary multiplicand M four times to the left and subtracting M shifted left once.

## Slide 21
Hardware for booth algorithm
Figure : Booth algorithm for multiplication of signed 2's complement numbers.
The two bits of multiplier in Qn and Qn+1 are inspected . If the two bits are equal to 10 it means that the first 1 in a string of 1’s has been encountered.
The final value of Qn+1 is the original sign bit of the multiplier and should not be taken as part of the product.

## Slide 22
Figure : Hardware for Booth algorithm

## Slide 23
Example : (-9) x ( - 13) = + 117 BR=10111 (multiplicand) and QR=10011 (multiplier)

## Slide 24
Q. Multiply the two numbers 23 and -9 by using the Booth's multiplication algorithm.
Here, BR = 23 = (010111) and QR= -9 = (110111)
Qn Qn + 1 | BR= 0 1 0 1 1 1 BR' + 1 = 1 0 1 0 0 1 Operation | AC | QR | Qn + 1 SC
 | Initially | 000000 | 110111 | 0 6
1 0 | Subtract BR | 101001 |  | 
 |  | 101001 |  | 
 | ashr | 110100 | 111011 | 1 5
1 1 | ashr | 111010 | 011101 | 1 4
1 1 | ashr | 111101 | 001110 | 1 3
0 1 | Addition BR | 010111 |  | 
 |  | 010100 |  | 
 | ashr | 001010 | 000111 | 0 2
1 0 | Subtract BR | 101001 |  | 
 |  | 110011 |  | 
 | ashr | 111001 | 100011 | 1 1
1 1 | ashr | 111100 | 110001 | 1 0

## Slide 25
Qn + 1 = 1, it means the output is negative.
Hence, 23 * -9 = 2's complement of 111100110001 => (00001100111)
Solve
Q. Multiply 3 x 5 using booth algorithm.
Q. Multiply -5 x 4 using booth algorithm.
Q. Multiply (-10) *(-4) using Booth's algorithm.

## Slide 26
The multiplication of the two binary numbers can be done with one micro-operation by means of a combinational circuit that forms the product bits all at once. This is a fast way of multiplying two numbers since all it takes is the time for the signals to propagate through the gate that form the multiplication array.
Figure : 2-bit by 2-bit array multiplier
Array multiplier

## Slide 27
Consider the multiplication of two 2-bit numbers as shown in Figure. The multiplicand bits are b1 and b0, the multiplier bits are a1 and a0, and the product is c3 c2 c1 c0.
This is identical to an AND operation and can be implemented with an AND gate. the first partial product is formed by means of two AND gates.
The second partial product is formed by multiplying a1 by b1 b0 and is shifted one position to the left. The two partial products are added with two half-adder (HA) circuits.
A combinational circuit binary multiplier with more bits can be constructed in a similar fashion.
For j multiplier bits and k multiplicand bits we need j x k AND gates and (j - 1) k-bit adders to produce a product of j + k bits.

## Slide 28
Figure : 4-bit by 3-bit array multiplier

## Slide 29
Division Algorithm
Division of two fixed-point binary numbers in signed magnitude representation is done with paper and pencil by a process of successive compare ,shift ,and subtract operations.
Figure : Example of binary division, 448/17

## Slide 30
Hardware Implementation for Signed-Magnitude Data
When the division is implemented in a digital computer, it is convenient to change the process slightly. Instead of shifting the divisor to the right, the dividend, or partial remainder, is shifted to the left, thus leaving the two numbers in the required relative position. Subtraction may be achieved by adding A to the 2's complement of B. The information about the relative magnitudes is then available from the end-carry.
Register EAQ is now shifted to the left with 0 inserted into Q, and the previous value of E lost.
Restoring Method: The reason for the name is that the partial remainder is restored by adding the divisor to the negative difference. Two other methods are available for dividing numbers, the Comparision method and the Nonrestoring method.
No restoring method B is not added if the difference is negative but instead, the negative difference is shifted left and then B is added.

## Slide 31
Divide operation
Hardware Algorithm (Restoring Algorithm)
The dividend AQ and the divisor is B . The sign of the result is transferred into Qs to be part of the quotient.
The sequence counter SC to specify the number of bits in the quotient.
If A >= B, the divide-overflow flip-flop DVF is set and the operation is terminated prematurely. If A < B, no divide overflow occurs so the value of the dividend is restored by adding B to A .
This is restoring step

## Slide 32
The division o f the magnitudes starts by shifting the dividend in A Q to the left with the high-order bit shifted into E. If the bit shifted into E =1, EA > B so B is subtracted from EA and Qn is set to 1.
If E=0, the divisor is subtracted by adding its 2's complement value and the carry is transferred into E .If E = 1, it signifies that A >=B; therefore, Qn is set to 1. If E = 0, it signifies that A < B and the original number is restored by adding B to A and we leave a 0 in Qn .
This process is repeated again with register A holding the partial remainder. After n - 1 times, the quotient magnitude is formed in register Q and the remainder is found in register A . The quotient sign is in Qs and the sign of the remainder in As

## Slide 33
Figure :Example of binary division with digital hardware.
Example : 448/17

## Slide 34
Non-restoring division Algorithm

## Slide 35
First the registers are initialized with corresponding values (Q = Dividend, B= Divisor, A = 0, SC = number of bits in dividend)
Step2: Check the sign bit of register A
If it is 1 shift left content of AQ and perform A = A+B, otherwise shift left AQ and perform A = A-B (means add 2’s complement of M to A and store it to A)
Again the sign bit of register A
If sign bit is 1 Qn become 0 otherwise Qn become 1 (Qn means least significant bit of register Q)
Decrements value of SC by 1
If SC is not equal to zero go to Step 2 otherwise go to next step
If sign bit of A is 1 then perform A = A+B
Register Q contain quotient and A contain remainder

## Slide 36
Example: 7/3

## Slide 37
Q. Divide 11/3 using non-restoring division
Q. Divide 5/3 using non-restoring division