## Slide 1: Basic computer organization and design
1

## Slide 2: Contents
  Instruction Code, Operation Code, Stored Program Concept
  Registers and memory of Basic Computer, Common Bus System for Basic Computer.
  Instruction Format, Instruction Set Completeness, Control Unit of Basic Computer, Control Timing Signals
  Instruction Cycle of Basic computer, Determining Type of Instruction,
  Memory Reference Instructions, Input-Output Instructions, Program Interrupt & Interrupt Cycle.
  Description and Flowchart of Basic Computer
2

## Slide 3: Introduction
The organization of the computer is defined by its internal register, the timing and control structure, and the set of instructions that it uses.
The internal organization of a digital system is defined by the sequence of
microoperations it performs on data stored in its registers.
Every different processor type has its own design (different registers, buses,
microoperations, machine instructions, etc.)
Modern processor is a very complex device
It contains
  Many registers
  Multiple arithmetic units, for both integer and floating point calculations
  The ability to pipeline several consecutive instructions to speed executi3on

## Slide 4
However, to understand how processors work, we will start with a simplified processor model
This is similar to what real processors were like ~25 years ago
M. Morris Mano introduces a simple processor model he calls the Basic Computer
We will use this to introduce processor organization and the relationship
of the RTL model to the higher level computer processor

## Slide 5
The basic computer
The Basic Computer has two components, a processor and memory
The memory has 4096 words in it
  4096 = 212, so it takes 12 bits to select a word in memory
Each word is 16 bits long

## Slide 6
Instructions
A computer instruction is a binary microoperations for the computer.
code that specifies a sequence of
Instruction codes together with data are stored in memory.
The computer reads each instruction from memory, the CPU reads the next instruction from memory and places it in in ( Instruction Register (IR)) a control register.
The control then interprets the binary code of the instruction and proceeds to execute it by issuing a sequence of microoperations.
Every computer has its own unique instruction set.

## Slide 7
Instruction Format
A computer instruction is often divided into two parts
  An opcode ( Operation Code) is the portion of a machine language instruction that specifies the operation for that instruction. also known as instruction machine code, instruction code, instruction syllable.
  The operation code of an instruction is a group of bits that define such operations as add, subtract, multiply, shift, and complement.
  An address that specifies the registers and/or locations in memory to use for that operation
In the Basic Computer, since the memory contains 4096 (= 212) words, we needs 12 bit to specify which memory address this instruction will use
In the Basic Computer, bit 15 of the instruction specifies the addressing mode
(0: direct addressing, 1: indirect addressing)

## Slide 8
Since the memory words, and hence the instructions, are 16 bits long, It consists of a 3-bit operation code, a 12-bit address, and an indirect address mode bit designated by I. the mode bit is 0 for a direct and 1 for an indirect address.

## Slide 9
Stored Program Organization
The simplest way to organize a computer is to have one processor register and instruction code format with two parts.
The first part specifies the operation to be performed and the second
specifies and address.
The memory address tells the control where to find an operand in memory. This operand is read from memory and used as the data to be operated on together with the data stored in the processor register.
Figure below depicts this type of organization. Instructions are stored in one section of memory and a data in another.
For a memory unit with 4096 words we need 12 bits to specify an address
since 212 = 4096.

## Slide 10
If we store each instruction code in one 16-bit memory word, we have available four bits for the operation code (abbreviated as opcode) to specify one out of 16 possible operation and 12 bits to specify the address of an operand.
The control reads a 16-bit instruction from the program portion of memory. It uses the 12 bit address part of the instruction to read and 16 bit operand
from the data portion of memory. It then executes the operation specified by the operation code.
Figure : Stored program organization.

## Slide 11
Computer that have a single processor register usually assign to it the name accumulator and label it AC. The operation is performed with the memory operand and the content of AC.
If an operation in an instruction code does not need and operand from memory, the rest of the bits in the instruction can be used for other purposes.
For example, operations such as clear AC, complement AC, and increment
AC operate on data stored in the AC register.

## Slide 12: Addressing Modes
Figure : Demonstration of direct and indirect address.
field of an can represent
The address instruction either
  Direct address
the data to use
address: the in memory of
(the
address of the operand),
or
Indirect address: the address in memory of
the address in memory of the data to use
0
ADD
457
22
Operand
457
1
ADD
300
35
1350
300
Operand
1350
+
AC
+
AC
Direct addressing
Indirect addressing

## Slide 13
A direct address instruction is shown in figure : b It is placed in address 22 in memory. The I bit is 0, so the instruction is recognized as a direct address instruction. The opcode specifies an ADD instruction, and the address part is the binary equivalent of 457. The control finds the operand in memory at address 457 and adds it to the content of AC.
The instruction in address 35 shown in figure : c has a mode bit I = 1. Therefore, it is recognized as an indirect address instruction. The address part is the binary equivalent of 300. The control goes to address 300 to find the address instruction needs two references to memory to fetch and
operand. The address of the operand in this case is 1350. The operand found in address 1350 is then added to the content of AC.
Effective Address(EA) is the location where operand is present , or as the target address for a branch-type instruction

## Slide 14: Basic Computer Registers and Memory
Computer instructions are normally stored in consecutive memory locations and are executed sequentially one at a time.
The control reads an instruction from a specific address in memory and executes it. It then continues by reading the next instruction in sequence and executes it, and so on. This type of instruction sequencing needs a counter to calculate the address of the next instruction after execution of the current
instruction is completed.
The computer needs processor registers for manipulating data and a register for holding a memory address.
The memory unit has a capacity of 4096 words and each word contains 16 bits. Twelve bits of an instruction word are needed to specify the address of an operand.

## Slide 15
A processor has many registers to hold instructions, addresses, data, etc
The data register (DR) holds the operand read from memory. The accumulator (AC) register is a general-purpose processing register.
The instruction read from memory is placed in the instruction register (IR). The temporary register (TR) is used for holding temporary data during the processing
The processor has a register, the Program Counter (PC) that holds the memory address of the next instruction to be read from memory after the current instruction is executed. Since, the memory in the Basic Computer only has 4096 locations, the PC only needs 12 bits

## Slide 16
In a direct or indirect addressing, the processor needs to keep track of what locations in memory it is addressing: The Address Register (AR) is used for this
The Input Register (INPR) holds an 8 bit character gotten from an input device
The Output Register (OUTR) holds an 8 bit character to be send to an output
device

## Slide 17
Register symbol | Number of bits | Register name | Function
DR | 16 | Data Register | Holds memory operand
AR | 12 | Address Register | Holds address for memory
AC | 16 | Accumulator | Processor register
IR | 16 | Instruction Register | Holds instruction code
PC | 12 | Program Counter | Holds address of instruction
TR | 16 | Temporary Register | Holds temporary data
INPR | 8 | Input Register | Holds input character
OUTR | 8 | Output Register | Holds output character
Table : List of Registers for the Basic Computer

## Slide 18
11
0
PC
15 0
IR
15 0
TR
OUTR
15 0
DR
15 0
AC
11 0
AR
INPR
7 0 7 0
Memory 4096 x 16
CPU
Figure : Basic computer registers and memory.

## Slide 19: Common Bus System
The basic computer has eight registers, a memory unit, and a control unit. Paths must be provided to transfer information from one register to another and between memory and register.
The registers in the Basic Computer are connected using a bus
This gives a savings in circuitry over complete connections between registers
The outputs of seven registers and memory are connected to the common
bus.
Three control lines, S2, S1, and S0 control which register the bus selects as its input.
For example, the number along the output of DR is 3. The 16-bit outputs
of DR are placed on the bus lines when S2S1S0 = 011 since this is the binary
value of decimal 3.
19

## Slide 21
S2
S1 S0
Bus
Memory unit 4096 x 16
LD INR CLR
Address
Write Read
AR
LD INR CLR
PC
LD INR CLR
DR
LD INR CLR
AC
ALU
E
INPR
IR
LD
LD INR CLR
TR
OUTR
Clock
7
1
2
3
4
5
6
LD
16-bit common bus
Figure : Basic computer registers connected to a common bus.

## Slide 22
LOAD | A | AC = M[A]
ADD | B | AC = AC + M[B]
STORE | T | M[T] = AC
LOAD | C | AC = M[C]
ADD | D | AC = AC + M[D]
MUL | T | AC = AC * M[T]
STORE | X | M[X] = AC
Example:
One Address Instructions Expression: X = (A+B)*(C+D)
AC is accumulator M[] is any memory location M[T] is temporary location

## Slide 23: Basic Computer Instructions
The basic computer has three instruction code formats. Each format has 16 bits. The operation code (opcode) part of the instruction contains three bits and the meaning of the remaining 13 bits depends on the operation code encountered.
A memory-reference instruction uses 12 bits to specify and address and one bit to specify the addressing mode I. I is equal to 0 for direct address and to 1 for indirect address.
The register reference instructions are recognized by the operation code 111 with a 0 in the leftmost bit (bit 15) of the instruction.
A register-reference instruction specifies an operation on or a test of the AC register. An operand from memory is not needed; therefore, the other 12 bits are used to specify the operation or test to be executed.

## Slide 24
Similarly, an input output instruction does not need a reference to memory and is recognized by the operation code 111 with a 1 in the leftmost bit of the instruction. The remaining 12 bits are used to specify the type of input-output operation or test performed.
The type of instruction is recognized by the computer control from the
four bits in positions 12 through 15 of the instruction.
If the three opcode bits in positions 12 through 14 are not equal to 111, the instruction is a memory-reference type and the bit in position 15 is taken as the addressing mode I. If the 3-bit opcode is equal to 111, control then inspects the bit in position 15.
If this bit is 0, the instruction is a register - reference type.
If the bit is 1, the instruction is an input-output type.
Note that the bit in position 15 of the instruction code is designated by the symbol I but is not used as a mode bit when the operation code is equal to 111.

## Slide 25
I | Opcode | Address
15
14
12 11
0
0 | 1 | 1 | 1 | Register operation
15
12 11
0
1 | 1 | 1 | 1 | I/O operation
15
12 11
0
Figure : Basic computer instruction formats.
(a) Memory-Reference Instructions (Opcode = 000 ~ 110)
(b) Register-Reference Instruction
(OP-code = 111, I = 0)
(c) Input-Output Instructions
(OP-code =111, I = 1)

## Slide 26
26
Table : Basic Computer Instruction

## Slide 27
Register- reference instructions
Register-reference instructions are recognized by the control when D7 = 1 and I = 0.
These instructions use bits 0 through 11 of the instruction code to specify
one of 12 instructions. These 12 bits are available in IR(0-11). were also transferred to AR during time T2
Execution starts with timing signal T3
r = D7 IT3 => Register Reference Instruction
Bi = IR(i) , i=0,1,2,...,11.[bit in IR(0-11) that specifies the operation]
They

## Slide 28
45
Table: Execution of Register –Reference instructions
 | r: rB11: rB10: rB9: rB8: rB7: rB6: rB5: rB4: rB3: rB2: rB1: rB0: | SC  0 | Clear SC
CLA |  | AC  0 | Clear AC
CLE |  | E  0 | Clear E
CMA |  | AC  AC’ | Complement AC
CME |  | E  E’ | Complement E
CIR |  | AC  shr AC, AC(15)  E, E  AC(0) | Circulate right
CIL |  | AC  shl AC, AC(0)  E, E  AC(15) | Circulate left
INC |  | AC  AC + 1 | Increment AC
SPA |  | if (AC(15) = 0) then (PC  PC+1) | Skip if positive
SNA |  | if (AC(15) = 1) then (PC  PC+1) | Skip if negative
SZA |  | if (AC = 0) then (PC  PC+1) | Skip if A C zero
SZE |  | if (E = 0) then (PC  PC+1) | Skip if E zero
HLT |  | S  0 (S is a start-stop flip-flop) | Halt computer

## Slide 29
Memory - Reference Instructions
The table below lists the seven memory-reference instructions.
The decoded output D, for i = 0,1, 2, 3, 4, 5, and 6 from the operation decoder that belongs effective address to each instruction is included in the table.
The effective address of the instruction is in the address register AR and was
placed there during timing signal T2 when I = 0, or during timing signal T3
when I=1.
The symbolic description of each instruction is specified in the table in terms of register transfer notation. The actual execution of the instruction in the bus system will require a sequence of microoperations.
The execution of MR instruction starts with T4

## Slide 30
AND to AC
This is an instruction that performs the AND logic operation on pairs of bits in AC and the memory word specified by the effective address. The result of the operation is transferred to AC . The microoperations that execute this instruction are:
D0T4: | DR  M[AR] | //Read operand
D0T5: | AC  AC  DR, SC  0 | //AND with AC
Symbol AND ADD LDA STA BUN BSA ISZ | Operation Decoder D0 D1 D2 D3 D4 D5 D6 | Symbolic Description AC  AC  M[AR] AC  AC + M[AR], E  Cout AC  M[AR] M[AR]  AC PC  AR M[AR]  PC, PC  AR + 1 M[AR]  M[AR] + 1, if M[AR] + 1 = 0 then PC  PC+1
Table : Memory-Reference Instructions

## Slide 31
D2T5: AC  DR, SC  0
//Load AC with DR
ADD to AC
This instruction adds the content of the memory word specified by the effective address to the value of AC . The sum is transferred into AC and the output carry Cout is transferred to the E (extended accumulator) flip-flop. The microoperations needed to execute this instruction are
D1T4: DR  M[AR] //Read operand
D1T5: AC  AC + DR, E  Cout, SC  0 //Add to AC and store carry
in E
LDA: Load to AC
This instruction transfers the memory word specified by the effective address to
AC . The microoperations needed to execute this instruction are
D2T4: DR  M[AR] //Read operand

## Slide 32
49
STA: Store AC
This instruction stores the content of AC into the memory word specified by
the effective address. Since the output of AC is applied to the bus and the data
input of memory is connected to the bus, we can execute this instruction with one microoperation
D3T4: M[AR]  AC, SC  0 //store data into memory location
BUN: Branch Unconditionally
PC is incremented at time T1 to prepare it for the address of the next instruction in the program sequence. The BUN instruction allows the programmer to specify an instruction out of sequence and we say that the program branches (or jumps) unconditionally. The instruction is executed with one microoperation:
D4T4: PC  AR, SC  0 //Branch to specified address

## Slide 33: BSA: Branch and Save Return Address
D5T4:M[AR]  PC,AR  AR + 1//save return address and increment AR
D5T5: PC  AR, SC  0 //load PC with AR
This is shown in part (a) of the figure. The BSA instruction performs the following numerical operation:
M[135]  21, PC  135 + 1 = 136
shown in part (b) of the figure.
Memory
The result of this operation is
(b) Memory, PC after execution
0 | BSA | 135
Next instruction |  | 
21 |  | 
Subroutine |  | 
1 | BUN | 135
0 | BSA | 135
Next instruction |  | 
Subroutine |  | 
1 | BUN | 135
20
PC = 21
AR = 135
136
(a) Memory, PC, AR at time T4
20
21
135
PC = 136
Memory
Figure : Example of BSA instruction execution.

## Slide 34
ISZ: Increment and Skip-if-Zero
This instruction increments the word specified by the effective address, and if
the incremented value is equal to 0, PC is incremented by 1.
It is not possible to increment a word inside the memory, it is necessary to read the word into DR, increment DR, and store the word back into memory. This is done with the following sequence of microoperations:
D6T4: | DR  M[AR] | //load data into DR | 
D6T5: | DR  DR + 1 | //increment data | 
D6T4: | M[AR]  DR, | if (DR = 0) then (PC  PC + 1), | SC  0

## Slide 35
Memory-reference instruction
DR  M[AR]
DR  M[AR]
DR  M[AR]
M[AR]  AC
SC  0
AND
ADD
LDA
STA
AC  AC  DR
SC  0
AC  AC + DR
E  Cout SC  0
AC  DR
SC  0
D 0T
4
D 1T
4
D 2T
4
D 3T
4
D T
0 5
D T
1 5
D T
2 5
PC  AR
SC  0
M[AR]  PC
AR  AR + 1
DR  M[AR]
BUN
BSA
ISZ
D 4T
4
D 5T
4
D 6T
4
DR  DR + 1
D 5T
5
D 6T
5
PC  AR SC  0
M[AR]  DR If (DR = 0)
then (PC  PC + 1)
SC  0
D 6T
6
Figure : Flowchart for memory-reference instructions.

## Slide 36
57
Input-output instructions
Input and output instructions are needed for transferring information to and from AC register, for checking the flag bits, and for controlling the interrupt facility.
Input-output instructions have an operation code 1111 and are recognized by the
control when D7 = 1 and I = 1.The remaining bits of the instruction specify the
particular operation.
The control functions and microoperations for the input-output instructions are listed in Table. D7 I T3 = p (common to all input-output instructions)
IR(i) = Bi [bit in IR (6-ll) that specifies the instruction]
 | p: | SC  0 | Clear SC
INP | pB11: | AC(0-7)  INPR, FGI  0 | Input char. to AC
OUT | pB10: | OUTR  AC(0-7), FGO  0 | Output char. from AC
SKI | pB9: | if(FGI = 1) then (PC  PC + 1) | Skip on input flag
SKO | pB8: | if(FGO = 1) then (PC  PC + 1) | Skip on output flag
ION | pB7: | IEN  1 | Interrupt enable on
IOF | pB6: | IEN  0 | Interrupt enable off

## Slide 37: Instruction set completeness
27
•
Examples: loading the AC(LDA), storing the accumulator (STA)
A computer should have a set of instructions so that the user can construct machine language programs to evaluate any function that is known to be computable.
The set of instructions are said to be complete if the computer includes a sufficient number of instructions in each of the following categories:
  Functional Instructions
    Arithmetic, logic, and shift instructions
    Example: ADD, complement AC(CMA), increment the accumulator AC (INC), circulate the AC right (CIR), circulate the accumulator left ( CIL), AND, clear AC(CLA)
  Transfer Instructions
    Data transfers between the main memory and the processor registers

## Slide 38
28
Control Instructions
  Program sequencing and control
  Example: BUN, BSA, ISZ
  The branch instructions BUN, BSA, and ISZ, together with the four skip instructions, provide capabilities for program control and checking of status conditions.
Input/Output Instructions
  Input and output
  Example: INP, OUT
  The input (INP) and output (OUT) instructions cause information to be transferred between the computer and external devices.

## Slide 39
The timing for all registers in the basic computer is controlled by a master clock generator.
The clock pulses are applied to all flip-flops and registers in the system, including the flip-flops and registers in the control unit.
The clock pulses do not change the state of a register unless the register is enabled by a control signal.
The control signals are generated in the control unit and provide control inputs for the multiplexers in the common bus, control inputs in processor registers, and microoperations for the accumulator.
Control Unit: Control unit (CU) of a processor translates from machine instructions to the control signals for the microoperations that implement them.
Timing and Control Unit

## Slide 40
Control units are implemented in one of two ways: hardwired control and microprogrammed control.
Hardwired control:
  The control logic is implemented with gates, flip-flops, decoders, and other digital circuits.
  It has the advantage that it can be optimized to produce a fast mode of operation.
  Requires changes in the wiring among the various components if the design has to be modified or changed, i.e. modification very difficult.
  Adding new feature is difficult.
  Expensive ,high error and used in RISC processor.
29

## Slide 41: Microprogrammed control:
30
The Control information is stored in a control memory. The control memory is programmed to initiate the required sequence of microoperations.
In the microprogrammed control, any required changes or modifications can
be done by updating the microprogram in control memory.
Slow ,cheap
Used in CISC processor.
………………………………………………………………………………..
The block Diagram of the hardware control unit is shown in figure below. It consists of two decoders, a sequence counter, and a number of control logic gates.
An instruction read from memory is placed in the instruction register (IR)

## Slide 42
15
Instruction register (IR)
14 13 12 11 - 0
3 x 8 decoder
7 6 5 4 3 2 1 0
I
D 0
15 14 . . . . 2 1 0
4 x 16
decoder
Control
signals
4-bit sequence counter (SC) |  |  |  | 
Increment (INR) Clear (CLR)
Clock
Other inputs
D 7
T15
T0
Combinational
Control
logic
31
Figure : Hardwired Control organization.

## Slide 43
In an instruction register, instruction read from memory is sored where it is divided into three parts the I bit, the operation code and bits 0 through 11. The operation code in bits12 through 14 are decoded with a 3 x 8 decoder.
The eight outputs of the decoder are designated by the binary value of the corresponding operation code. Bit 0 through 11 are applied to the control logic gates.
The 4 bit sequence counter can count in binary from 0 through 15. The outputs of the counter are decoded into 16 timing signals T0 through T15.The sequence counter SC can be incremented or cleared synchronously.

## Slide 44
Timing Signals
Most of the time the counter is incremented to provide the sequence of timing
signals out of the 4 x 16 decoder. Once in awhile, the counter is cleared to 0,
causing the next active timing signal to be T0.
Example, consider the case where SC is incremented to provide timing signals T0, T1, T2, T3, and T4 in sequence. At time T4 SC is cleared to 0 if decoder output D3 is active. This is expressed symbolically by the statement D3T4: SC  0

## Slide 45
Figure : Example of control timing signals
T0
T1
T2
T3
T4
T0
Clock
T0 T1 T2 T3 T4 D3
CLR SC

## Slide 46
Figure: Functioning of Microprogrammed Control Unit

## Slide 47
The inputs (IR, ALU flags, clock) and outputs (control signals). The control unit functions as follows:
  To execute an instruction, the sequencing logic unit issues a READ command to the control memory.
  The word whose address is specified in the control address register is read into the control buffer register.
  The content of the control buffer register generates control signals
and next-address information for the sequencing logic unit.
  The sequencing logic unit loads a new address into the control address register based on the next-address information from the control buffer register and the ALU flags.

## Slide 48: Instruction Cycle
A program residing in the memory unit of the computer consists of a sequence of
instructions. The program is executed in the computer by going through a cycle for each instruction.
In Basic Computer, a machine instruction is executed in the following cycle:
  Fetch an instruction from memory
  Decode the instruction
  Read the effective address from memory if the instruction has an indirect address
  Execute the instruction
Upon the completion of step 4, the control goes back to step 1 to fetch, decode, and execute the next instruction. This process continues indefinitely unless a HALT instruction is encountered.
Note: Every different processor has its own (different) instruction cycle
37

## Slide 49
Fetch and Decode
Initially, the program counter PC is loaded with the address of the first
instruction in the program.
The sequence counter SC is cleared to 0, providing a decoded timing signal T0,T1,T2, and so on.
The microoperations for the fetch and decode phases can be specified by
the following register transfer statements.
T0: AR←PC
T1: IR←M[AR],PC←PC +1
T2: D0, ….D7←decode IR (12-14) ,AR←IR (0-11) ,I←IR(15)

## Slide 50
Since only AR is connected to the address inputs of memory, it is necessary to transfer the address from PC to AR during the clock transition associated with timing signal T0.
The instruction read from memory is then placed in the instruction register IR with the clock transition associated with timing signal T1.
At the same time, PC is incremented by one to prepare it for the
address of the next instruction in the program.
At time T2, the operation code in IR is decoded, the indirect bit is transferred to flip-flop I, and the address part of the instruction is transferred to AR.
Note: The sequence counter SC incremented after each clock pulse to produce the sequence T0, T1 and T2.

## Slide 51
S2
S0
S1 Bus
7
Memory
unit
Address
Read
AR
LD
PC
INR
IR
LD
Clock
1
2
5
Common bus
T1
T0
Figure : Register transfers for the fetch phase.

## Slide 52
T0 to achieve the following connection:
Place the content of PC onto the bus by making the bus selection inputs S2S1S0 equal to 010.
Transfer the content of the bus to AR by enabling the LD input of AR.
The next clock transition initiates the transfer from PC to AR since T0=1. In order to implement the second statement
T1: IR <- M[AR], PC <- PC + 1
it is necessary to use timing signal T1 to provide the following connections in the bus system.
Enable the read input of memory.
Place the content of memory onto the bus by making S2 S1S0 = 1ll.
Transfer the content of the bus to IR by enabling the LD input of IR
Increment PC by enabling the INR input of PC .

## Slide 53: Determine the type of instruction
= 0 (direct)
AR  PC
Start
SC  
T0
IR  M[AR], PC  PC + 1
T1
Decode Opcode in IR(12-14),
AR  IR(0-11), I  IR(15)
T2
D7
= 0 (Memory-reference)
(Register or I/O) = 1
I
I
Execute register-reference
instruction
SC  0
Execute input-output instruction
SC  0
AR  M[AR]
Nothing
= 0 (register)
(I/O) = 1
(indirect) = 1
T3
T3
T3
T3
Execute memory-reference
instruction
SC  0
T4
42
Figure : Flowchart for instruction cycle (initial configuration).

## Slide 54
The timing signal that is active after the decoding is T3. During time T3 the control unit determines the type of instruction that was just read from memory.
The flowchart of figure above presents an initial configuration for the instruction cycle and shows how the control determines the instruction type after the decoding.
We determine that if D7 =1, the instruction must be a register-reference or input output type. If D7 = 0, the operation code must be one of the other seven values 000 through 110, specifying a memory reference instruction.
The three instruction types are subdivided into four separate paths. The selected operation is activated with the clock transition associated with timing
signal T3. This can be symbolized as follows: D7 I T3: AR +M[AR]
D7 I’T3: Nothing
D7 I’T3: Execute a register-reference instruction D7 I T3 : Execute an input-output instruction

## Slide 55: Input-Output and Interrupt
53
Instructions and data stored in memory must come from some input device. Computational results must be transmitted to the user through some output device. Commercial computers include many types of input and output devices.
Input-Output Configuration
The terminal sends and receives serial information. Each quantity of
information has eight bits of an alphanumeric code.
The two registers communicate with a communication interface serially and with the AC in parallel.
The serial information from the keyboard is shifted into the input register INPR . The serial information for the printer is stored in the output register
OUTR.

## Slide 56
Input-output
Terminal
Serial
communication
interface
Computer registers and flip-flops
Printer
Keyboard
Receiver interface
Transmitter interface
FGO
OUTR
AC
INPR
FGI
Figure : Input-output configuration

## Slide 57
INPR Input register - 8 bits, OUTR Output register - 8 bits, FGI Input flag - 1 bit, FGO Output flag - 1 bit, IENInterrupt enable - 1 bit
Initially, the input flag FGI is cleared to 0. When a key is struck in the keyboard, an 8-bit alphanumeric code is shifted into INPR and the input flag FGI is set to 1. As long as the flag is set, the information in INPR cannot be changed by striking another key. The computer checks the flag bit; if it is 1, the information from INPR is transferred in parallel into AC and FGI is cleared to 0. Once the flag is cleared, new information can be shifted into INPR by striking another key.
The output register OUTR works similarly but the direction of information flow is reversed. Initially, the output flag FGO is set to 1. The computer checks the flag bit; if it is 1, the information from AC is transferred in parallel to OUTR and FGO is cleared to 0. The output device accepts the coded information, prints the corresponding character, and when the operation is completed, it sets FGO to 1.

## Slide 58: Program controlled data transfer
-- CPU --
-- I/O Device --
Start Input
FGI  0
FGI=0
AC  INPR
More Character
END
Start Output
FGO=0
More Character
END
OUTR  AC |  | 
FGO  0 |  | 
AC  Data
yes
no
yes
no
FGI=0
FGO=1
yes
yes
no
no

## Slide 59
Program Interrupt
The process of communication just described is referred to as programmed control transfer. The computer keeps checking the flag bit, and when it finds it set, it initiates an information transfer.
Consider a computer that can transfer information at a maximum rate of 10 characters per second. This is equivalent to one character every 100,000µs. Two instructions are executed when the computer checks the flag bit and decides not to transfer the information. This means that at the maximum rate, the computer will check the flag 50000 times between each transfer. The computer is wasting time while checking the flag instead of doing some other useful processing task.
The interrupt enable flip-flop IEN can be set and cleared with two instructions. When IEN is cleared to 0 the flags cannot interrupt the computer.

## Slide 60
When IEN is set to 1 the computer can be interrupted. These two instructions provide the programmer with the capability of making a decision as to whether or not to use the interrupt facility.

## Slide 61: Interrupt Cycle
R
=1
=0
Store return address in location 0 M[0]  PC
Branch to location 1
PC  1
IEN  0
R  0
Interrupt cycle
Instruction cycle
Fetch and decode
instructions
FGO
Execute instructions | 
 | R 
IEN
=1
=1
=1
=0
FGI
=0
=0
1
Figure : Flowchart for interrupt cycle

## Slide 62
Figure : Demonstration of the interrupt cycle
(b) After interrupt cycle
0 | BUN | 1120
Main Program |  | 
I/O Program |  | 
1 | BUN | 0
0
1
255
PC = 256
(a) Before interrupt
1120
256 |  | 
0 | BUN | 1120
Main Program |  | 
I/O Program |  | 
1 | BUN | 0
0
PC = 1
255
256
Memory
1120
Memory
The interrupt cycle is a HW
implementation of a branch and save return address operation.
At the beginning of the next
instruction cycle, the instruction that is read from memory is in address 1.
At memory address 1, the programmer
must store a
branch instruction that sends
the control to an interrupt service routine
The instruction that returns the
control to the original program
is "indirect BUN 0"

## Slide 63
Register Transfer Statements for Interrupt Cycle, The interrupt cycle is initiated after the last execute phase if the interrupt flip-flop R is equal to 1. This flip-flop is set to 1 if IEN = 1 and either FGI or FGO are equal to 1. This can happen with any clock transition except when timing signals T0, T1 or T2 are active.
T0T1T2 (IEN)(FGI + FGO): R  1
The fetch and decode phases of the instruction cycle must be modified: Replace T0, T1, T2 with R'T0, R'T1, R’T2
The interrupt cycle :
RT0:
RT1:
RT2:
AR  0, TR  PC
M[AR]  TR, PC  0
PC  PC + 1, IEN  0, R  0, SC  0

## Slide 64: Complete Computer Description
Design of Basic computer :
The basic computer consists of the following hardware components:
A memory unit with 4096 words of 16 bits each
Nine registers : AR, PC, DR, AC, IR, TR. OUTR, INPR, and SC
Seven flip-flop: I, S, E,R, IEN. FGI, and FGO
Two decoders: a 3 x 8 operation decoder and a 4 x 16 timing decoder
A 16 bit common bus.
Control logic gates.
Adder and logic circuit connected to the input of AC

## Slide 65: Flowchart
= 1 (I/O)
=0 (Register)
=1(Indirect)
=0 (Direct)
Start
SC  0, IEN  0, R  0
R
AR  PC
R’T0
IR  M[AR], PC  PC + 1
R’T1
AR  IR(0~11), I  IR(15)
D0...D7  Decode IR(12 ~ 14)
R’T2
AR  0, TR  PC
RT0
M[AR]  TR, PC  0
RT
1
PC  PC + 1, IEN  0 R  0, SC  0
RT2
D7
I
I
Execute I/O Instruction
Execute RR
Instruction
AR <- M[AR]
Idle
D7IT3
D7I’T3
D7’IT3
D7’I’T3
Execute MR Instruction
=0 (Instruction Cycle) =1 (Interrupt Cycle)
=1(Register or I/O)
=0 (Memory Ref)
D7’T4
Figure : Flowchart for computer operation.

## Slide 66
Fetch
Decode
Indirect
Interrupt
Memory-Reference AND
ADD
LDA
STA BUN BSA
ISZ
RT0: RT1: RT2:
D7IT3:
RT2:
D0T4: D0T5: D1T4: D1T5: D2T4: D2T5: D3T4: D4T4: D5T4: D5T5: D6T4: D6T5: D6T6:
AR  PC
IR  M[AR], PC  PC + 1
D0, ..., D7  Decode IR(12 ~ 14),
AR  IR(0 ~ 11), I  IR(15) AR  M[AR]
R  1
AR  0, TR  PC M[AR]  TR, PC  0
PC  PC + 1, IEN  0, R  0, SC  0
DR  M[AR]
AC  AC  DR, SC  0 DR  M[AR]
AC  AC + DR, E  Cout, SC  0 DR  M[AR]
AC  DR, SC  0
M[AR]  AC, SC  0
PC  AR, SC  0
M[AR]  PC, AR  AR + 1 PC  AR, SC  0
DR  M[AR] DR  DR + 1
M[AR]  DR, if(DR=0) then (PC  PC + 1), SC  0
T0T1T2(IEN)(FGI + FGO):
RT0:
RT1:

## Slide 67
Register-Reference
CLA CLE CMA CME CIR CIL INC SPA SNA SZA SZE HLT
Input-Output
INP OUT SKI SKO ION IOF
D7IT3 = r IR(i) = Bi
r: rB11: rB10:
rB9: rB8: rB7: rB6: rB5: rB4: rB3: rB2:
rB1: rB0:
D7IT3 = p IR(i) = Bi
p: pB11: pB10:
pB9: pB8: pB7: pB6:
(Common to all register-reference instr) (i = 0,1,2, ..., 11)
SC  0
AC  0
E  0
AC  AC E  E
AC  shr AC, AC(15)  E, E  AC(0) AC  shl AC, AC(0)  E, E  AC(15) AC  AC + 1
If(AC(15) =0) then (PC  PC + 1) If(AC(15) =1) then (PC  PC + 1) If(AC = 0) then (PC  PC + 1)
If(E=0) then (PC  PC + 1) S  0
(Common to all input-output instructions) (i = 6,7,8,9,10,11)
SC  0
AC(0-7)  INPR, FGI  0 OUTR  AC(0-7), FGO  0 If(FGI=1) then (PC  PC + 1) If(FGO=1) then (PC  PC + 1) IEN  1
IEN  0

## Slide 68
Control Logic Gates Inputs:
The inputs from the two decoders,
I flip-flop
IR-bits (0-11)
AC bits 0 -15 to check if AC = 0 and to detect the sign bit in AC(15)
DR bits 0 -15 to check if DR 0 and
the values of the seven flip-flops.
Outputs:
Signals to control the inputs of the nine registers
Signals to control the read and write inputs of memory
Signals to set, clear, or complement the flip-flops
Signals for 52, 51, and 50 to select a register for the bus
Signals to control the AC adder and logic circuit

## Slide 69: Control of registers and memory
The control inputs of the registers are LD (load), INR (increment), and CLR (clear). Suppose that we want to derive the gate structure associated
Address Register; AR, Scan all of the register transfer statements that change
the content of AR:
LD(AR) = R'T0 + R'T2 + D'7IT3 CLR(AR) = RT0
INR(AR) = D5T4
R’T0: AR  PC R’T2: AR  IR(0-11) D’7IT3: AR  M[AR] RT0: AR  0
D5T4: AR  AR + 1
LD(AR)
LD(AR)
LD(AR) CLR(AR)
INR(AR)

## Slide 70
69
AR
LD
INR
CLR
Clock
To bus
12
From bus
12
D'7 I
T 3
T 2
R T 0 D T 4
Figure : Control gates associated with AR.
where LD(AR) is the load input of AR, CLR(AR) is the clear input of AR, and INR(AR) is the increment input of AR . The control gate logic associated with AR is shown in Figure.
In a similar fashion we can derive the control gates for the other registers as well as the logic needed to control the read and write inputs of memory. The read operation is recognized from the symbol <-M[AR].
Read = R’T1 + D´7IT3 + (D0 + D1 + 02 + D6)T4

## Slide 71: Control of Flags
The control gates for the seven flip-flops can be determined in a similar
manner
IEN: Interrupt Enable Flag pB7: IEN  1 (I/O Instruction) pB6: IEN  0 (I/O Instruction)
RT2: IEN  0 (Interrupt) where, p = D7IT3 (Input/Output Instruction) and B, and B, are bits 7 and 6 of IR.
T3
D 7
I
J
K
Q
IEN
p
B 7
B 6
R T2
70
Figure : Control inputs for IEN.

## Slide 72: Control of Common Bus
71
The 16-bit common bus is controlled by the selection inputs S2, S1, and S0 The decimal number shown with each bus input specifies the equivalent binary number that must be applied to the selection inputs in order.
Each binary number is associated with a Boolean variable x1 through x7, corresponding to the gate structure that must be active in order to select the register or memory for the bus.
Table : Encoder for Bus Selection Circuit

## Slide 73
x1 x2 x3 x4 x5 x6 x7
Encoder
S 2
Multiplexer
S 1 bus select inputs
S 0
For example, to find the logic that makes x1 = I, we scan all register transfer statements that have AR as a source.
D4T4: PC  AR
D5T5: PC  AR
Therefore, the Boolean function for x1 is x1 = D4T4 + D5T5
Similarly, The data output from memory are selected for the bus when x7 = 1 and S2 S1 S0 = 1ll. The gate logic that generates x7 must also be applied to the read input of memory. Therefore, the Boolean function for x7 is the same as the one derived previously for the read operation.
x7 = R’T4 + D7’IT3+ (D0+ D1 + D2 + D6)T4
Figure :Encoder for bus selection inputs.

## Slide 74: Design of Accumulator Logic
16
16
8
Adder and logic circuit
16
AC
From DR
From INPR
Control gates
LD
INR
CLR
16
To bus
Clock
Figure : Circuits associated with AC.

## Slide 75
D0T5: AC  AC  DR D1T5: AC  AC + DR D2T5: AC  DR
pB11: AC(0-7)  INPR
AND with DR Add with DR Transfer from DR
Transfer from INPR Complement
Shift right Shift left Clear Increment
rB9: rB7 : rB6 :
AC  AC
AC  shr AC, AC(15)  E
AC  shl AC, AC(0)  E
rB11 : AC  0
rB5 : AC  AC + 1

## Slide 76: Control of AC register
AC
LD
INR
CLR
Clock
To bus
16
From Adder and Logic
16
AND
ADD
DR
INPR
COM
SHR
SHL
INC
B11
CLR
B11
r
B9
B7 B6
B5
p
D0 T 5 D1
D2
T 5
75
Gate structures for controlling the LD, INR, and CLR of AC show in below:
Figure : Gate structure for controlling the LD, INR, and CLR of AC.

## Slide 77: Adder and Logic circuit
AND
ADD
DR
INPR
COM
J
K
Q
AC(i)
LD
FA
C
From INPR
bit(i)
SHR
AC(i+1)
SHL
AC(i-1)
C i
DR(i)
AC(i)
i+1
I
i
76
Figure : One stage of adder and logic circuit.